## Slide 1
Logic Families

## Slide 2: Tutorial
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of Digital Logic Families
  Classify various logic families
  Describe essential prime implicants
  Recognize don’t care conditions
  Draw five variable K-map

## Slide 4: Topics
Digital Logic Families

## Slide 5
How many 74LS00 NAND gate inputs can be driven by a 74LS00 NAND gate outputs ?
Solution:
Refer to data sheet of 74LS00, the maximum values of
IOH = 0.4mA, IOL = 8mA, IIH = 20uA, and IIL = 0.4mA
Hence,
fan-out(high) = IOH(max) / IIH (max)=0.4mA/20uA=20
fan-out(low) = IOL(max) / IIL(max)=8mA/0.4mA=20,
the overall fan-out = fan-out(high) or fan-out(low) whichever is lower.
Hence, overall fan-out = 20
Worked Example

## Slide 6
Given the following parameters, calculate the noise margin of 74LS series
Solution:
High Level Noise Margin, VNH = VOH (min) - VIH (min)=2.7V-2.0V=0.7V
Low Level Noise Margin, VNL = VIL (max) - VOL (max)=0.8V-0.4V=0.4V
Worked Example

## Slide 7
Summary
An implicant is a product term in an SOP expression (or a sum term in POS expression)
  A prime implicant is an implicant that is not fully contained in some other larger implicant
  Don't care situations are often called incompletely specified functions
  K-maps can also be used for POS minimization