## Slide 1
Combinational Digital Circuit

## Slide 2: Lecture 34 Arithmetic circuits
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of Binary multipliers
  Acquire the knowledge of Ripple adders
  Describe BCD Decoder

## Slide 4: Topics
Binary Multipliers
Ripple Adders
BCD Decoder
Gray Decoder

## Slide 5
Multiplication of binary numbers is performed in the same way as multiplication of decimal numbers
The multiplicand is multiplied by each bit of the multiplier, starting from the least significant bit
Each such multiplication forms a partial product. Successive partial products are shifted one position to the left
The final product is obtained from the sum of the partial products
  Binary Multipliers

## Slide 6
To see how a binary multiplier can be implemented with a combinational circuit, consider the multiplication of two 2-bit numbers
  Binary Multipliers
Multiplication of two bit numbers
Two bit multiplier circuit

## Slide 7
The multiplicand bits are B1 and B0, the multiplier bits are A1 and A0, and the product is C3 C2 C1 C0
The first partial product is formed by multiplying B1 B0 by A0
The multiplication of two bits such as A0 and B0 produces a 1 if both bits are 1; otherwise, it produces a 0
Therefore, the partial product can be implemented with AND gates as shown in the diagram
The second partial product is formed by multiplying B1B0 by A1 and shifting one position to the left
The two partial products are added with two half-adder (HA) circuits
  Binary Multipliers

## Slide 8
A combinational circuit binary multiplier with more bits can be constructed in a similar fashion
For J multiplier bits and K multiplicand bits, we need (J * K) AND gates and (J – 1) K- bit adders to produce a product of (J + K) bits
As a second example, consider a multiplier circuit that multiplies a binary number represented by four bits by a number represented by three bits
Let the multiplicand be represented by B3 B2 B1 B0 and the multiplier by A2 A1 A0
  Binary Multipliers

## Slide 9
Since K=4 and J=3, we need 12 AND gates and two 4-bit adders to produce a product of seven bits
  Binary Multipliers
Four-bit by three-bit
binary multiplier

## Slide 10
Multiple full adder circuits can be cascaded in parallel to add an N-bit number
For an N- bit parallel adder, there must be N number of full adder circuits
A ripple carry adder is a logic circuit in which the carry-out of each full adder is the carry in of the succeeding next most significant full adder
In a ripple carry adder the sum and carry out bits of any half adder stage is not valid until the carry in of that stage occurs
  Ripple carry adder

## Slide 11
  Ripple carry adder
4 bit ripple carry adder

## Slide 12
Assume addition of two operands A and B
where ,
A= A3 A2 A1 A0
B=B3 B2 B1 B0
For example: A= 1 0 1 1 +
B= 1 1 0 1
---------------
A+B= 1 1 0 0 0 = Cout S3 S2 S1 S0
From the example above it can be seen that we are adding 3 bits at a time sequentially until all bits are added
  Ripple carry adder

## Slide 13
  Ripple carry adder
4 Bit ripple adder

## Slide 14
BCD-to-decimal decoder converts each BCD code to its decimal equivalent
BCD decoder
BCD to decimal decoder
Truth table for BCD to decimal decoder

## Slide 15
The technique employed is very similar to the one used in developing the 3-line-to-8-line decoder
Assuming active high outputs are required, Table lists the decoding functions for BCD-to-decimal decoder
BCD decoder
BCD to Decimal decoder

## Slide 16
BCD decoder
DECIMAL DIGIT | BCD INPUTS |  |  |  | LOGIC FUNCTIONS
0 | 0 | 0 | 0 | 0 | A’3A’2A’1A’0
1 | 0 | 0 | 0 | 1 | A’3A’2A’1A0
2 | 0 | 0 | 1 | 0 | A’3A’2A1A’0
3 | 0 | 0 | 1 | 1 | A’3A’2A1A0
4 | 0 | 1 | 0 | 0 | A’3A2A’1A’0
5 | 0 | 1 | 0 | 1 | A’3A2A’1A0
6 | 0 | 1 | 1 | 0 | A’3A2A1A’0
7 | 0 | 1 | 1 | 1 | A’3A2A1A0
8 | 1 | 0 | 0 | 0 | A3A’2A’1A’0
9 | 1 | 0 | 0 | 1 | A3A’2A’1A0
Decoding functions for BCD-to-decimal decoder

## Slide 17
BCD decoder
BCD to decimal decoder

## Slide 18
BCD to seven segment decoder
BCD to 7 segment decoder truth table
BCD to 7 segment decoder Block diagram

## Slide 19
BCD to seven segment decoder
BCD to 7 Segment block diagram

## Slide 20
Gray decoder
Gray to binary decoder
Gray to binary truth table
Gray to binary K-map

## Slide 21
Gray to binary decoder
Gray to binary decoder

## Slide 22
Summary
For J multiplier bits and K multiplicand bits, we need (J * K) AND gates and (J – 1) K- bit adders to produce a product of (J + K) bits
A ripple carry adder is a logic circuit in which the carry-out of each full adder is the carry in of the succeeding next most significant full adder
A BCD to decimal decoder can be realized using a 4:16 decoder or by using logic circuits
A BCD to seven segment decoder is used to drive a seven segment display
A gray to binary decoder can be realized by finding out the Boolean expression using K-map