## Slide 1
Basics of Memories

## Slide 2: Lecture 40 Different types of memory
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Classify different types of memory
  Acquire the knowledge of RAM and its types
  Acquire the knowledge of ROM and its types

## Slide 4: Topics
Different types of memory
RAM and its types
ROM and its types

## Slide 5
Memory Arrays
Computer Architecture and Organization

## Slide 6
Levels of the Memory Hierarchy
Computer Architecture and Organization
Part of The On-chip CPU Datapath
ISA 16-128 Registers
One or more levels (Static RAM):
Level 1: On-chip 16-64K
Level 2: On-chip 256K-2M
Level 3: On or Off-chip 1M-16M
Registers
Cache
Level(s)
Main Memory
Magnetic Disc
Optical Disk or Magnetic Tape
Farther away from
the CPU:
Lower Cost/Bit
Higher Capacity
Increased Access
Time/Latency
Lower Throughput/
Bandwidth
Dynamic RAM (DRAM)
256M-16G
Interface:
SCSI, RAID,
IDE, 1394
80G-300G
CPU

## Slide 7
Main Memory
Most of the main memory in a general purpose computer is made up of RAM integrated circuits chips, but a portion of the memory may be constructed with ROM chips
RAM– Random Access memory
  Integated RAM are available in two possible operating modes, Static and Dynamic
ROM– Read Only memory

## Slide 8
Memory components are extremely useful for many purposes in addition to storage. There are two basic types of memory:
  Read/write memory (RAM)
  Read-only memory (ROM)
Memory Types

## Slide 9
  Static Memory: For static memory, the memory cells are simple flip-flops or bistable multivibrator with two stable states so that the cells can hold their state permanently as long as the power is applied
  Dynamic Memory (DRAM): DRAM chips have much simpler memory cells in which the state of the memory cell is indicated by the presence or absence of stored charge in a capacitor. As time passes, charge leakage occurs and the information is lost even if power is left on
  Pseudo-static Memory: These chips are actually dynamic memory. They act like static memory because the refresh circuitry is provided inside the chip
RAM Types

## Slide 10
Applications of ROM: There are many applications of ROMs, some of which include:
  Permanent information storage
  Code conversion
  Multiple output function generation
Read-Only Memory
Read-Only Memory (ROM):
  It is read only: it can be read from but not written to.
  It is not volatile: Its contents are not lost when power is off.

## Slide 11
  Types of ROM:
    ROM
    PROM (Programmable read-only memory) : An example of a PROM is the P2764A production EPROM chip.
    EPROM (Erasable programmable read-only memory) : More versatile and popular type of ROM .EPROMs are ideal for experimentation and development when the final edition of the program is not yet available.
    EEPROM (Electrically erasable programmable read-only memory) : Information can be directly and dynamically erased electrically under program control.
Read-Only Memory

## Slide 12
Summary
Most of the main memory in a general purpose computer is made up of RAM integrated circuits chips
Integrated RAM are available in two possible operating modes, Static and Dynamic
There are two basic types of memory:
  Read/write memory (RAM)
  Read-only memory (ROM)