## Slide 1
Basics of Memories

## Slide 2: Lecture 41 Structure of RAM
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Classify different types of memory
  Acquire the knowledge of RAM and its types
  Acquire the knowledge of ROM and its types

## Slide 4: Topics
Memory Definitions
Memory Organization
Memory Block Diagram
RAM Integrated Circuits
Static RAM Cell

## Slide 5: Memory Definitions
Memory ─ A collection of storage cells together with the necessary circuits to transfer information to and from them
Memory Organization ─ the basic architectural structure of a memory in terms of how data is accessed
Random Access Memory (RAM) ─ a memory organized such that data can be transferred to or from any cell (or collection of cells) in a time that is not dependent upon the particular cell selected
Memory Address ─ A vector of bits that identifies a particular memory element (or collection of elements)

## Slide 6: Memory Definitions (Continued)
Typical data elements are:
  bit ─ a single binary digit
  byte ─ a collection of eight bits accessed together
  word ─ a collection of binary bits whose size is a typical unit of access for the memory. It is typically a power of two multiple of bytes (e.g., 1 byte, 2 bytes, 4 bytes, 8 bytes, etc.)
Memory Data ─ a bit or a collection of bits to be stored into or accessed from memory cells
Memory Operations ─ operations on memory data supported by the memory unit. Typically, read and write operations over some data element (bit, byte, word, etc.)

## Slide 7: Memory Organization
Organized as an indexed array of words. Value of the index for each word is the memory address
Often organized to fit the needs of a particular computer architecture
  Intel 8080 – (8-bit predecessor to the 8086 and the current Intel processors) used a 16-bit address to address 65,536 8-bit bytes

## Slide 8: Memory Block Diagram
A basic memory system is shown here:
k address lines are decoded to address 2k words of memory
Each word is n bits
Read and Write are single control lines defining the simplest of memory operations
n Data Input Lines
k Address Lines
Read
Write
n Data Output Lines
Memory
Unit
2k Words
n Bits per Word
k
1
1
n
n

## Slide 9: Memory Organization Example
Example memory contents:
  A memory with 3 address bits & 8 data bits has:
  k = 3 and n = 8 so 23 = 8 addresses labeled 0 to 7
  23 = 8 words of 8-bit data
Memory Address
Binary Decimal
Memory
Content
0 0 0 0
1 0 0 0 1 1 1 1
0 0 1 1
1 1 1 1 1 1 1 1
0 1 0 2
1 0 1 1 0 0 0 1
0 1 1 3
0 0 0 0 0 0 0 0
1 0 0 4
1 0 1 1 1 0 0 1
1 0 1 5
1 0 0 0 0 1 1 0
1
1 0 6
0 0 1 1 0 0 1 1
1 1 1 7
1 1 0 0 1 1 0 0

## Slide 10: Basic Memory Operations
Memory operations require the following:
  Data ─ data written to, or read from, memory as required by the operation
  Address ─ specifies the memory location to operate on. The address lines carry this information into the memory. Typically: n bits specify locations of 2n words
  An operation ─ Information sent to the memory and interpreted as control information which specifies the type of operation to be performed. Typical operations are READ and WRITE. Others are READ followed by WRITE and a variety of operations associated with delivering blocks of data. Operation signals may also specify timing info

## Slide 11: Basic Memory Operations (continued)
Read Memory ─ an operation that reads a data value stored in memory:
  Place a valid address on the address lines
  Wait for the read data to become stable
Write Memory ─ an operation that writes a data value to memory:
  Place a valid address on the address lines and valid data on the data lines
  Toggle the memory write control line

## Slide 12: Overview
Memory definitions
Random Access Memory (RAM)
Static RAM (SRAM) integrated circuits
  Cells and slices
  Cell arrays and coincident selection
Arrays of SRAM integrated circuits
Dynamic RAM (DRAM) integrated circuits
DRAM Types
  Synchronous (SDRAM)
  Double-Data Rate (DDR SRAM)
  RAMBUS DRAM (RDRAM)
Arrays of DRAM integrated circuits

## Slide 13: RAM Integrated Circuits
Types of random access memory
  Static – information stored in latches
  Dynamic – information stored as electrical charges on capacitors
    Charge “leaks” off
    Periodic refresh of charge required
Dependence on Power Supply
  Volatile – loses stored information when power turned off
  Non-volatile – retains information when power turned off

## Slide 14: Overview
Memory definitions
Random Access Memory (RAM)
Static RAM (SRAM) integrated circuits
  Cells and slices
  Cell arrays and coincident selection
Arrays of SRAM integrated circuits
Dynamic RAM (DRAM) integrated circuits

## Slide 15: Static RAM Cell
Array of storage cells used to implement static RAM
Storage Cell
  SR Latch
  Select input for control
  Dual Rail Data Inputs B and B
  Dual Rail Data Outputs C and C
Select
B
RAM cell
C
C
B
S
R
Q
Q

## Slide 16: Static RAM Bit Slice
Represents all circuitry that is required for 2n 1-bit words
  Multiple RAM cells
  Control Lines:
    Word select i – one for each word
    Bit Select
  Data Lines:
    Data in
    Data out

## Slide 17: 2n-Word  1-Bit RAM IC
Read/
To build a RAM IC from a RAM slice, we need:
  Decoder :decodes the n address lines to 2n word select lines
  A 3-state buffer
  on the data output permits RAM ICs to be combined into a RAM with c  2n words
Word select
Read/Write
logic
Data in
Data out
Write
Bit
select
(b) Block diagram
RAM cell
RAM cel
l
RAM cell
Data input
Chip select
Read/Write
Data
output
A
3
A
2
A
1
A
0
2
3
2
2
2
1
2
0
4-to-16
Decoder
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
3
A
2
A
1
A
0
Data
input
Data
output
(a) Symbol
Read/
Write
Memory
enable
16 x
1
RAM

## Slide 18: Cell Arrays and Coincident Selection
Memory arrays can be very large =>
  Large decoders
  Large fanouts for the bit lines
  The decoder size and fanouts can be reduced by approximately by using a coincident selection in a 2-dimensional array
  Uses two decoders, one for words and one for bits
  Word select becomes Row select
  Bit select becomes Column select
See next slide for example
  A3 and A2 used for Row select
  A1 and A0 for Column select

## Slide 19: Cell Arrays and Coincident Selection (continued)
Data input
Read/Write
X
X
X
A
1
A
0
RAM cell
0
RAM cell
4
RAM cell
8
RAM cell
12
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
1
RAM cell
5
RAM cell
9
RAM cell
13
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
2
RAM cell
6
RAM cell
10
RAM cell
14
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
3
RAM cell
7
RAM cell
11
RAM cell
15
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
Column
decoder
2-to-4 Decoder
with enable
2
1
2
0
0
1
Column select
2
Enable
3
Chip select
Data
output
Row
select
Row decoder
A
2
A
3
X
2-to-4
Decoder
2
0
2
1
1
2
3
0

## Slide 20: RAM ICs with > 1 Bit/Word
Word length can be quite high
To better balance the number of words and word length, use ICs with > 1 bit/word

## Slide 21: 8 Words x 2 bits Memory 2 Data input bits 2 Data output bits Row select selects 4 rows Column select selects 2 pairs of columns
Contd..

## Slide 22: Making Larger Memories (more words)
Using the CS lines, we can make larger memories from smaller ones by tying all address, data, and R/W lines in parallel, and using the decoded higher order address bits to control CS
Using the 4-Word by 1-Bit memory from before, we construct a 16-Word by 1-Bit memory. 

## Slide 23: Making Wider Memories (more bits)
To construct wider memories from narrow ones, we tie the address and control lines in parallel and keep the data lines separate.
For example, to make a 4-word by 4-bit memory from 4, 4-word by 1-bit memories 
Note: Both 16x1 and 4x4 memories take 4-chips and hold 16 bits of data

## Slide 24
Summary
Memory ─ A collection of storage cells together with the necessary circuits to transfer information to and from them
Types of random access memory
  Static – information stored in latches
  Dynamic – information stored as electrical charges on capacitors
Using the 4-Word by 1-Bit memory from before, we construct a 16-Word by 1-Bit memory