## Slide 1
Basics of Memories

## Slide 2: Lecture 42 Structure of ROM
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of Non-volatile
  Describe the Structure of ROM
  Differentiate various types of ROM

## Slide 4: Topics
  Non-volatile memory
Structure of ROM
Failure Modes of EEPROM
Comparison

## Slide 5: Non-volatile Retains the stored information even when not powered
Electrically Addressed
    ROM
      PROM
      EAROM
      EPROM
      EEPROM
    Flash memory (NOR and NAND)
Mechanically Addressed System
    Tape
    Hard disk
    Optical disk (CD, DVD)
    Magnetic Disk (Floppy Disk)

## Slide 6: ROM Read-only memory
Stored-program computer requires some form of non-volatile storage to store the initial program that runs when the computer is powered on or otherwise begins execution (a process known as bootstrapping, often abbreviated to "booting" or "booting up")
Read-only memory (ROM), also known as firmware, is an integrated circuit programmed with specific data when it is manufactured. ROM chips are used not only in computers, but in most other electronic items as well.

## Slide 7: PROM Programmable Read Only Memory
Programmable read-only memory (PROM) or field programmable read-only memory (FPROM) is a form of digital memory where the setting of each bit is locked by a fuse or antifuse. Such PROMs are used to store programs permanently. The key difference from a strict ROM is that the programming is applied after the device is constructed.
Creating ROM chips totally from scratch is time-consuming and very expensive in small quantities. For this reason, mainly, developers created a type of ROM known as programmable read-only memory (PROM). Blank PROM chips can be bought inexpensively and coded by anyone with a special tool called a programmer.
Advantages
    Reliability
    Stores data permanently
    Moderate price
    Built using integrated circuits, rather than discrete components.
    Fast: speed is between 35ns and 60ns.
Notes: PROM chips have a grid of columns and rows just as ordinary ROMs do. The difference is that every intersection of a column and row in a PROM chip has a fuse connecting them. A charge sent through a column will pass through the fuse in a cell to a grounded row indicating a value of 1. Since all the cells have a fuse, the initial (blank) state of a PROM chip is all 1s. To change the value of a cell to 0, you use a programmer to send a specific amount of current to the cell. The higher voltage breaks the connection between the column and row by burning out the fuse. This process is known as burning the PROM.
PROMs can only be programmed once. They are more fragile than ROMs. A jolt of static electricity can easily cause fuses in the PROM to burn out, changing essential bits from 1 to 0. But blank PROMs are inexpensive and are great for prototyping the data for a ROM before committing to the costly ROM fabrication process.

## Slide 8: EPROM Erasable Programmable Read Only Memory
It is an array of floating-gate transistors individually programmed by an electronic device that supplies higher voltages than those normally used in electronic circuits. Once programmed, an EPROM can be erased only by exposing it to strong ultraviolet light
Working with ROMs and PROMs can be a wasteful business. Even though they are inexpensive per chip, the cost can add up over time. Erasable programmable read-only memory (EPROM) addresses this issue. EPROM chips can be rewritten many times. Erasing an EPROM requires a special tool that emits a certain frequency of ultraviolet (UV) light. EPROM's are configured using an EPROM programmer that provides voltage at specified levels depending on the type of EPROM used
EPROM's are easily recognizable by the transparent fused quartz window in the top of the package, through which the silicon chip can be seen, and which permits UV light during erasing
Notes: Once again we have a grid of columns and rows. In an EPROM, the cell at each intersection has two transistors. The two transistors are separated from each other by a thin oxide layer. One of the transistors is known as the floating gate and the other as the control gate. The floating gate's only link to the row (wordline) is through the control gate. As long as this link is in place, the cell has a value of 1. To change the value to 0 requires a curious process called Fowler-Nordheim tunneling. Tunneling is used to alter the placement of electrons in the floating gate. An electrical charge, usually 10 to 13 volts, is applied to the floating gate. The charge comes from the column (bitline), enters the floating gate and drains to a ground.
This charge causes the floating-gate transistor to act like an electron gun. The excited electrons are pushed through and trapped on the other side of the thin oxide layer, giving it a negative charge. These negatively charged electrons act as a barrier between the control gate and the floating gate. A device called a cell sensor monitors the level of the charge passing through the floating gate. If the flow through the gate is greater than 50 percent of the charge, it has a value of 1. When the charge passing through drops below the 50-percent threshold, the value changes to 0. A blank EPROM has all of the gates fully open, giving each cell a value of 1.
To rewrite an EPROM, you must erase it first. To erase it, you must supply a level of energy strong enough to break through the negative electrons blocking the floating gate. In a standard EPROM, this is best accomplished with UV light at a frequency of 253.7. Because this particular frequency will not penetrate most plastics or glasses, each EPROM chip has a quartz window on top of it. The EPROM must be very close to the eraser's light source, within an inch or two, to work properly.
An EPROM eraser is not selective, it will erase the entire EPROM. The EPROM must be removed from the device it is in and placed under the UV light of the EPROM eraser for several minutes. An EPROM that is left under too long can become over-erased. In such a case, the EPROM's floating gates are charged to the point that they are unable to hold the electrons at all.

## Slide 9: EEPROM Electrically Erasable Programmable Read Only Memory
Though EPROMs are a big step up from PROMs in terms of reusability, they still require dedicated equipment and a labor-intensive process to remove and reinstall them each time a change is necessary
Also, changes cannot be made incrementally to an EPROM; the whole chip must be erased
Notes: Serial bus devices
Most common serial interface types are SPI, I²C and 1-Wire. These three interfaces require between 2 and 4 controls signals for operation, resulting in a memory device in an 8 pin (or less) package.
The serial EEPROM typically operates in three phases: OP-Code Phase, Address Phase and Data Phase. The OP-Code is usually the first 8-bits input to the serial input pin of the EEPROM device (or with most I²C devices, is implicit); followed by 8 to 24 bits of addressing depending on the depth of the device, then data to be read or written.
Each EEPROM device typically has its own set of OP-Code instructions to map to different functions. Some of the common operations on SPI EEPROM devices are:
  Write Enable (WREN)
  Write Disable (WRDI)
  Read Status Register (RDSR)
  Write Status Register (WRSR)
  Read Data (READ)
  Write Data (WRITE)
Other operations supported by some EEPROM devices are:
  Program
  Sector Erase
  Chip Erase commands
Parallel bus devices
Parallel EEPROM devices typically have an 8-bit data bus and an address bus wide enough to cover the complete memory. Most devices have chip select and write protect pins. Some microcontrollers also have integrated parallel EEPROM.
Operation of a parallel EEPROM is simple and fast when compared to serial EEPROM, but these devices are larger due to the higher pin count (28 pins or more) and have been decreasing in popularity in favor of serial EEPROM or Flash.

## Slide 10
Electrically erasable programmable read-only memory (EEPROM) chips remove the biggest drawbacks of EPROMs. In EEPROMs:
The chip does not have to removed to be rewritten
The entire chip does not have to be completely erased to change a specific portion of it
Changing the contents does not require additional dedicated equipment
Here are different types of electrical interfaces to EEPROM devices. Main categories of these interface types are :
    Serial bus
    Parallel bus
How the device is operated depends on the electrical interface
Contd..

## Slide 11: Failure Modes of EEPROM
There are two limitations of stored information; endurance, and data retention
During rewrites, the gate oxide in the floating-gate transistors gradually accumulates trapped electrons
The electric field of the trapped electrons adds to the electrons in the floating gate, lowering the window between threshold voltages for zeros vs ones. After sufficient number of rewrite cycles, the difference becomes too small to be recognizable, the cell is stuck in programmed state, and endurance failure occurs
The manufacturers usually specify minimal number of rewrites being 10000000 or more
Notes: Purpose behind FLASH Memory
An obvious extension of flash memory would be as a replacement for hard disks. Flash memory does not have the mechanical limitations and latencies of hard drives, so the idea of a solid-state drive, or SSD, is attractive when considering speed, noise, power consumption, and reliability.
There remain some aspects of flash-based SSDs that make the idea unattractive. Most importantly, the cost per gigabyte of flash memory remains significantly higher than that of platter-based hard drives. Although this ratio is decreasing rapidly for flash memory, it is not yet clear that flash memory will catch up to the capacities and affordability offered by platter-based storage. Still, research and development is sufficiently vigorous that it is not clear that it will not happen, either
There is also some concern that the finite number of erase/write cycles of flash memory would render flash memory unable to support an operating system. This seems to be a decreasing issue as warranties on flash-based SSDs are approaching those of current hard drives.

## Slide 12
During storage, the electrons injected into the floating gate may drift through the insulator, especially at increased temperature, and cause charge loss, reverting the cell into erased state. The manufacturers usually guarantee data retention of 10 years
When larger amounts of static data are to be stored (such as in USB flash drives) a specific type of EEPROM such as flash memory is more economical than traditional EEPROM devices
Contd..

## Slide 13
EEPROM
Electrically byte-erasable
Lower reliability
Higher cost
Lower density
ROM
High density
Reliable
Low cost
Suitable for stable code production
DRAM
High density
Low cost
High speed
High power
FLASH
Full-Feature
Memory Solution
Flash Memory
Low-cost, high density
High speed architecture
Lower power
High reliability
DRAM
ROM
EPROM
EEPROM
Non-volatile
FLASH
Updateable
High Density
Comparison

## Slide 14
Summary
Read-only memory (ROM), also known as firmware, is an integrated circuit programmed with specific data when it is manufactured
Creating ROM chips totally from scratch is time-consuming and very expensive in small quantities
  EPROM's are easily recognizable by the transparent fused quartz window in the top of the package
  When larger amounts of static data are to be stored a specific type of EEPROM such as flash memory is more economical than traditional EEPROM devices