## Slide 1
Introduction to Digital Electronics

## Slide 2: Lecture 5 Number System
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Convert binary to decimal conversion
  Acquire the knowledge of octal to decimal conversion
  Convert hexadecimal to decimal conversion
  Acquire the knowledge of decimal to binary conversion

## Slide 4: Topics
Conversion Among Bases
Binary to Decimal conversion
Octal to Decimal conversion
Hexadecimal to Decimal conversion
Decimal to Binary conversion

## Slide 5
Conversion Among Bases
Hexadecimal
Decimal
Octal
Binary
The possibilities:

## Slide 6: Quick Example
2510 = 110012 = 318 = 1916
Base
Decimal to Decimal (just for fun)
Hexadecimal
Decimal
Octal
Binary

## Slide 7: Contd..
12510 => 5 x 100 = 5 2 x 101 = 20 1 x 102 = 100 125
Base
Weight

## Slide 8: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 9: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 10: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 11: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 12: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 13: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 14: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1

## Slide 15: Decimal to Binary
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012
Example

## Slide 16
Summary
Multiply each bit by 2n, where n is the “weight” of the bit
The weight is the position of the bit, starting from 0 on the right
Add the results
Multiply each bit by 8n, where n is the “weight” of the bit
The weight is the position of the bit, starting from 0 on the right
Add the results
Binary to Decimal
Octal to Decimal