## Slide 1
Introduction to Digital Electronics

## Slide 2: Tutorial
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of Binary addition
  Compute Binary multiplication

## Slide 4: Topics
Multiplying powers
Binary Addition
Binary Multiplication
Fractions

## Slide 5: Review – multiplying powers
For common bases, add powers
26  210 = 216 = 65,536
or…
26  210 = 64  210 = 64k
ab  ac = ab+c

## Slide 6: Binary Addition (1 of 2)
Two 1-bit values
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10
“two”

## Slide 7: Binary Addition (2 of 2)
Two n-bit values
  Add individual bits
  Propagate carries
  E.g.,
10101 21 + 11001 + 25 101110 46
1
1

## Slide 8: Multiplication (1 of 3)
Decimal (just for fun)
35 x 105 175 000 35 3675

## Slide 9: Multiplication (2 of 3)
Binary, two 1-bit values
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 10: Multiplication (3 of 3)
Binary, two n-bit values
  As with decimal values
  E.g.,
1110 x 1011 1110 1110 0000 1110 10011010

## Slide 11
Fractions
Decimal to decimal (just for fun)
3.14 => 4 x 10-2 = 0.04 1 x 10-1 = 0.1 3 x 100 = 3 3.14

## Slide 12
Fractions
Binary to decimal
10.1011 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0.0 1 x 21 = 2.0 2.6875

## Slide 13
Fractions
Decimal to binary
3.14579
.14579 x 2 0.29158 x 2 0.58316 x 2 1.16632 x 2 0.33264 x 2 0.66528 x 2 1.33056
etc.
11.001001...

## Slide 14
Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
29.8 |  |  | 
 | 101.1101 |  | 
 |  | 3.07 | 
 |  |  | C.82

## Slide 15
Exercise – Convert ...
Decimal | Binary | Octal | Hexa- decimal
29.8 | 11101.110011… | 35.63… | 1D.CC…
5.8125 | 101.1101 | 5.64 | 5.D
3.109375 | 11.000111 | 3.07 | 3.1C
12.5078125 | 1100.10000010 | 14.404 | C.82

## Slide 16
Summary
A binary addition is creating a sum of (1 + 1 = 10) i.e. 0 is written in the given column and a carry of 1 over to the next column
Binary addition was shown to be very simple to implement
Binary multiplication is similar to decimal multiplication
It is simpler than decimal multiplication because only 0s and 1s are involved