## Slide 1
Introduction to Digital Electronics

## Slide 2: Lecture 11 Logic Gates
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Describe Binary Logic
  Acquire the knowledge of Truth Tables
  Acquire the knowledge of Logic Gates
  Recognize Logic Gate Symbols and Behavior
  Acquire the knowledge of Logic Diagrams and Expressions

## Slide 4: Topics
Binary Logic
Truth Tables
Logic Function Implementation
Logic Gates
Logic Gate Symbols and Behavior
Logic Diagrams and Expressions

## Slide 5
Binary Logic
Definition of Binary Logic
  Binary logic consists of binary variables and a set of logical operations
  The variables are designated by letters of the alphabet, such as A, B, C, x, y, z, etc, with each variable having two and only two distinct possible values: 1 and 0,
  Three basic logical operations: AND, OR, and NOT
AND is denoted by a dot (·)
OR is denoted by a plus (+)
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable

## Slide 6
Binary Logic

## Slide 7
Examples:
Y = A . B is read “Y is equal to A AND B.”
Z = X + Y is read “z is equal to x OR y.”
X = Ā is read “X is equal to NOT A.”
Notation Examples

## Slide 8: Operator Definitions
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0
=
0
1
=

## Slide 9
Truth Tables
Truth table - A tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0
1
1
0
X
NOT
X
Z
=

## Slide 10: Logic Function Implementation
Using Switches
  For inputs:
    logic 1 is switch closed
    logic 0 is switch open
  For outputs:
    logic 1 is light on
    logic 0 is light off
  NOT uses a switch such that:
    logic 1 is switch open
    logic 0 is switch closed
Switches in parallel => OR
Switches in series => AND

## Slide 11: Logic Gates
In the earliest computers, switches were opened and closed by magnetic fields produced by energizing coils in relays. The switches in turn opened and closed the current paths
Later, vacuum tubes that open and close current paths electronically replaced relays
Today, transistors are used as electronic switches that open and close current paths

## Slide 12: Logic Gates
Implementation of logic gates with transistors
Transistor or tube implementations of logic functions are called logic gates or just gates
Transistor gate circuits can be modeled by switch circuits

## Slide 13: Logic Gate Symbols and Behavior
Logic gates have special symbols:

## Slide 14: Logic Diagrams and Expressions
Boolean equations, truth tables and logic diagrams describe the same function
Truth tables are unique; expressions and logic diagrams are not. This gives flexibility in implementing functions
X
Y
F
Z
Logic Diagram
Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F
×
+
=

## Slide 15
Summary
Binary logic consists of binary variables and a set of logical operations
Three basic logical operations are: AND, OR, and NOT
  A tabular listing of the values of a function for all possible combinations of values on its arguments is called truth table
  Boolean equations, truth tables and logic diagrams describe the same function