## Slide 1
Concepts of Boolean Algebra

## Slide 2: Lecture 15 Boolean Analysis of Logic Circuits
Lecture delivered by:
Deepak V.

## Slide 3: Topics
Boolean Analysis of Logic Circuits
Constructing a Truth Table for a Logic Circuit

## Slide 4: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge Boolean Analysis of Logic Circuits
  Compile a Truth Table for a Logic Circuit

## Slide 5
Boolean Analysis of Logic Circuits
Boolean algebra provides a concise way to express the operation of a logic circuit formed by a combination of logic gates so that the output can be determined for various combinations of input values.
Figure: A logic circuit showing the development of the Boolean expression for the output

## Slide 6
Boolean Analysis of Logic Circuits
To derive the Boolean expression for a given logic circuit, begin at the leftmost inputs and work toward the final output
The Boolean expression is determined as follows:
The expression for the left-most AND gate with inputs C and D is CD
The output of the left-most AND gate is one of the inputs to the OR gate and B is the other input. Therefore, the expression for the OR gate is B + CD
The output of the OR gate is one of the inputs to the right-most AND gate and A is the other input. Therefore, the expression for this AND gate is
A(B + CD), which is the final output expression for the entire circuit.

## Slide 7
Constructing a Truth Table for a Logic Circuit
Once the Boolean expression for a given logic circuit has been determined, a truth table that shows the output for all possible values of the input variables can be developed
  By considering the previous circuit as the example
  A(B+CD)
There are four variables, hence 16 (24) combinations of values are possible

## Slide 8
Constructing a Truth Table for a Logic Circuit
Evaluating the expression
  To evaluate the expression A(B+CD), first find the values of the variables that make the expression equal to 1 (using the rules for Boolean add & mult)
  In this case, the expression equals 1 only if A=1 and B+CD=1 because
  A(B+CD) = 1·1 = 1

## Slide 9
Evaluating the expression (cont’)
  Now, determine when B+CD term equals 1.
  The term B+CD=1 if either B=1 or CD=1 or if both B and CD equal 1 because
  B+CD = 1+0 = 1
  B+CD = 0+1 = 1
  B+CD = 1+1 = 1
The term CD=1 only if C=1 and D=1
Constructing a Truth Table for a Logic Circuit

## Slide 10
Evaluating the expression (cont’)
  Summary:
    When A=1 and B=1 regardless of the values of C and D
    When A=1 and C=1 and D=1 regardless of the value of B
  The expression A(B+CD)=0 for all other value combinations of the variables
Constructing a Truth Table for a Logic Circuit

## Slide 11
Putting the results in truth table format
When A=1 and B=1 regardless of the values of C and D
When A=1 and C=1 and D=1 regardless of the value of B
A(B+CD)=1
Constructing a Truth Table for a Logic Circuit
INPUTS |  |  |  | OUTPUT
A | B | C | D | A(B+CD)
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 12
TRUTH TABLE FOR F1=xyz’, F2=x+y’z, F3=x’y’z+x’yz+xy’ and F4=xy’+x’z
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0
Contd..

## Slide 13
Contd..

## Slide 14
(c) F4 = xy’+x’z
F4
z
y
x
Implementation of Boolean Function with GATES
Contd..

## Slide 15
Summary
Boolean algebra provides a concise way to express the operation of a logic circuit formed by a combination of logic gates
Once the Boolean expression is determined, a truth table can be developed