## Slide 1
Concepts of Boolean Algebra

## Slide 2: Lecture 16 Simplification Using Boolean Algebra
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge Boolean Analysis of Logic Circuits
  Construct a Logic Circuit

## Slide 4: Topics
Simplification Using Boolean Algebra
Draw a Logic Circuit

## Slide 5
Simplification Using Boolean Algebra
A simplified Boolean expression uses the fewest gates possible to implement a given expression
Example
Using Boolean algebra techniques, simplify this expression:
AB + A(B + C) + B(B + C)

## Slide 6
Simplification Using Boolean Algebra
Solution
Step 1: Apply the distributive law to the second and third terms in the expression, as follows:
AB + AB + AC + BB + BC
Step 2: Apply rule 7 (BB = B) to the fourth term.
AB + AB + AC + B + BC
Step 3: Apply rule 5 (AB + AB = AB) to the first two terms.
AB + AC + B + BC
Step 4: Apply rule 10 (B + BC = B) to the last two terms.
AB + AC + B

## Slide 7
Step 5: Apply rule 10 (AB + B = B) to the first and third terms.
B+AC
At this point the expression is simplified as much as possible.
Simplification Using Boolean Algebra
Figure: Gate circuits for example above.

## Slide 8
Simplification Using Boolean Algebra

## Slide 9
Simplification Using Boolean Algebra

## Slide 10
(x + y’)z + x’
Simplification Using Boolean Algebra
Example

## Slide 11
The expression and circuit on the previous page are actually equivalent to the simplified ones below:
Simplification Using Boolean Algebra
x’ + z

## Slide 12
Simplification Using Boolean Algebra

## Slide 13
Simpler expressions yield simpler hardware
The resulting from the original and simplified expressions on the previous page

## Slide 14
Summary
A simplified Boolean expression uses the fewest gates possible to implement a given expression
The logic circuit can be minimised by using simplification methods