## Slide 1
Logic Families

## Slide 2: Lecture 29 Gate Characteristics
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of logic device pin-outs
  Explain gate characteristics
  Describe transistors as switches

## Slide 4: Topics
Gate Characteristics
Electrical Characteristics
Power Dissipation
Noise Margin

## Slide 5
Gate Characteristics
The inverter or NOT gate
  consider the characteristics of a simple inverting amplifier as shown below
  we normally use only the linear region

## Slide 6
An inverting amplifier cab be used as a logical inverter but using only the non-linear region
Gate Characteristics

## Slide 7
  An input values is choose to ensure that we are always outside of the linear region – as in (a)
  Unlike linear amplifiers, the circuits is used with a rapid transition between the non-linear regions – as in (b)
Gate Characteristics

## Slide 8: Characteristics: TTL and MOS
TTL stands for Transistor-Transistor Logic
  uses BJTs
MOS stands for Metal Oxide Semiconductor
  uses FETs
MOS can be classified into three sub-families:
  PMOS (P-channel)
  NMOS (N-channel)
  CMOS (Complementary MOS, most common)
Remember:

## Slide 9
Electrical Characteristics
The characteristics of digital logic families are usually compared by analyzing the circuit of the basic gate in each family
The most important parameters are:
Fan-out specifies the number of standard loads that the output can drive without impairing its normal operation.
A standard load is usually defined as the amount of current needed by an input of another similar gate of the same family.
Power dissipation is the power consumed by the gate
Propagation delay is the average transition delay time for the signal to propagate from input to output
Noise margin is the minimum external noise vo,ltage that causes an undesirable change in the circuit output

## Slide 10
Power Dissipation
Static
  I2R losses due to passive components, no input signal
Dynamic
  I2R losses due to charging and discharging capacitances through resistances, due to input signal

## Slide 11
Noise Margin
Manufacturers specify voltage limits to represent the logical 0 or 1
These limits are not the same at the input and output sides
  For example, a particular Gate A may output a voltage of 4.8V when it is supposed to output a HIGH but, at its input side, it can take a voltage of 3V as HIGH
In this way, if any noise should corrupt the signal, there is some margin for error

## Slide 12
Noise Margin
If noise in the circuit is high enough it can push a logic 0 up or drop a logic 1 down into the indeterminate or “illegal” region
The magnitude of the voltage required to reach this level is the noise margin
Noise margin for logic high is:
  NMH = VOHmin – VIHmin
VOHmin
VIHmin
VILmax
VOLmax
logic 0
logic 1
indeterminate
input voltage

## Slide 13
Noise Margin
Difference between the worst case output voltage of one stage and worst case input voltage of next stage
Greater the difference, the more unwanted signal that can be added without causing incorrect gate operation
NMhigh = VOHmin - VIHmin
NMlow = VILmax - VOLmax

## Slide 14
Noise immunity of a logic circuit refers to the circuit’s ability to tolerate noise voltages on its inputs.
A quantitative measure of noise immunity is called noise margin
High Level Noise Margin, VNH = VOH (min) - VIH (min)
Low Level Noise Margin, VNL = VIL (max) - VOL (max)
Noise Margin & Noise Immunity
Logic 1
Logic 0
Logic 0
Logic 1
VOH (min)
VOL (max)
VIH (min)
VIL (max)
VNH
VNL
Output Voltage Ranges
Input Voltage Ranges

## Slide 15
Further Important Characteristics
The propagation delay (tpd) which is the time taken for a change at the input to appear at the output
The fan-out, which is the maximum number of inputs that can be driven successfully to either logic level before the output becomes invalid

## Slide 16
Speed: Rise & Fall Times
Rise Time
  Time from 10% to 90% of signal, Low to High
Fall Time
  Time from 90% to 10% of signal, High to Low
rise time
10%
90%
90%
10%
fall time

## Slide 17
A logic gate always takes some time to change states
tPLH is the delay time before output changes from low to high
tPHL is the delay time before output changes from high to low
both tPLH & tPHL are measured between the 50% points on the input and output transitions
Speed: Propagation Delay
50%
Input
Output
0
0
tPHL
tPLH

## Slide 18
Speed (propagation delay) and power consumption are the two most important performance parameters of a digital IC.
A simple means for measuring and comparing the overall performance of an IC family is the speed-power product (the smaller, the better).
For example, an IC has
  an average propagation delay of 10 ns
  an average power dissipation of 5 mW
  the speed-power product = (10 ns) x (5 mW)
  = 50 picoJoules (pJ)
Speed-Power Product

## Slide 19
Logic Family Tradeoffs
Looking for the best speed/power product
tp and Pd are normally included in the data sheet for each device
Older logic families are the worst
CMOS is one of the best
FPGAs use CMOS

## Slide 20
Comparison of Logic Families

## Slide 21
Summary
An inverting amplifier cab be used as a logical inverter but using only the non-linear region
An input values is choosen to ensure that we are always outside of the linear region
  Unlike linear amplifiers, the circuits is used with a rapid transition between the non-linear regions
  The propagation delay (tpd) which is the time taken for a change at the input to appear at the output