## Slide 1
Combinational Digital Circuit

## Slide 2: Lecture 32 Multiplexers
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of Multiplexers
  Describe De-Multiplexers

## Slide 4: Topics
Multiplexers
De-Multiplexers

## Slide 5
  Multiplexers
A multiplexer is a combinational circuit that selects binary information from one of many input lines and directs it to a single output line
The selection of a particular input line is controlled by a set of selection lines
Normally, there are 2n input lines and n selection lines whose bit combinations determine which input is selected
For example, a two-to-one-line multiplexer connects one of two 1-bit sources to a common destination

## Slide 6
  Multiplexers
Two to one Multiplexer
In the figure below C is the select pin
X1 ,X0 are the input pins, Z is the output
When C=0, X0 is chosen as output
When C=1, X1 is chosen as output

## Slide 7
The circuit diagram for a two to one MUX using logic gates is shown below:
2:1 MUX using basic gates
  Multiplexers

## Slide 8
  Multiplexers
A 4:1 MUX has 4 inputs, one output and two select lines
4:1 MUX using basic gates
4:1 MUX Truth table

## Slide 9
Multiplexer circuits can be combined with common selection inputs to provide multiple-bit selection logic
As an illustration, a quadruple 2-to-1-line multiplexer is shown below
  Multiplexers
Quadruple two-to-one-line multiplexer

## Slide 10
A MUX can also be used to implement a Boolean function, the procedure is given below:
Implementing a Boolean function of n variables with a multiplexer that has n - 1 selection inputs:
      The first n - 1 variables of the function are connected to the selection inputs of the multiplexer
      The remaining single variable of the function is used for the data inputs
      If the single variable is denoted by z, each data input of the multiplexer will be z, z’,1, or 0.
  Multiplexers

## Slide 11
To demonstrate this procedure, consider the Boolean function
F (x, y, z) =
This function of three variables can be implemented with a four-to-one-line multiplexer
The two variables x and y are applied to the selection lines in that order
X is connected to the S1 input and y to the S0 input
The values for the data input lines are determined from the truth table of the function
When xy = 00, output F is equal to z because F = 0 when
z = 0 and F = 1 when z = 1
  Multiplexers

## Slide 12
  Multiplexers
Implementing a Boolean function with a multiplexer

## Slide 13
As a second example, consider the implementation of the Boolean function F (A, B, C, D) = Σ(1, 3, 4, 11, 12, 13, 14, 15)
This function is implemented with a multiplexer with three
selection inputs
A must be connected to selection input S2 so that A , B, and C correspond to selection inputs S2, S1, and S0, respectively
  Multiplexers

## Slide 14
  Multiplexers
Implementing a four-input function with a multiplexer

## Slide 15
A DEMUX is a digital switch with a single input (source) and a multiple outputs (destinations)
The select lines determine which output the input is connected to
DEMUX Types
   1-to-2 (1 select line)
   1-to-4 (2 select lines)
   1-to-8 (3 select lines)
   1-to-16 (4 select lines)
  De-Multiplexers

## Slide 16
  De-Multiplexers
Select
Lines
Input
(source)
Outputs
(destinations)
2N
1
N
DEMUX
A DEMUX has one input, 2n outputs and n select lines
De-Mux Block diagram

## Slide 17: Typical Application of a DEMUX
  De-Multiplexers
Single Source
Multiple Destinations
Selector
D0
D1
D2
D3
X
DEMUX
B | A | Selected Destination
0 | 0 | B/W Laser Printer
0 | 1 | Fax Machine
1 | 0 | Color Inkjet Printer
1 | 1 | Pen Plotter
B/W Laser
Printer
Color Inkjet
Printer
Pen
Plotter
Fax
Machine

## Slide 18
B | A | D0 | D1 | D2 | D3
0 | 0 | X | 0 | 0 | 0
0 | 1 | 0 | X | 0 | 0
1 | 0 | 0 | 0 | X | 0
1 | 1 | 0 | 0 | 0 | X
D0
D1
D2
D3
X
B A
DEMUX
  De-Multiplexers
1:4 De-mux Logic Diagram
1:4 De-mux Block Diagram
1:4 De-mux Truth table

## Slide 19
Summary
A multiplexer is a combinational circuit that selects binary information from one of many input lines and directs it to a single output line
Normally, there are 2n input lines and n selection lines in a MUX whose bit combinations determine which input is selected
A DEMUX is a digital switch with a single input (source) and a multiple outputs (destinations)
A DEMUX has one input, 2n outputs and n select lines