## Slide 1
Introduction to Digital Electronics

## Slide 2: Lecture 4 Number System
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of Positional-Value System
  List of the Various radix
  Distinguish between various number systems
  Acquire the knowledge of Data Organization

## Slide 4: Topics
Positional-Value System
Decimal Number System
Octal number system
Binary Digits
Hexadecimal number system
Common Powers
Binary Codes

## Slide 5
Positional-Value System
The value of a digit (“digit” from Latin word for finger) depends on its position

## Slide 6: Decimal Number System
Base (also called radix) = 10
  10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
5
1
2
7
4
10
1
0.1
100
0.01
500
10
2
0.7
0.04
d2*B2+d1*B1+d0*B0+d-1*B-1+d-2*B-2
(512.74)10

## Slide 7: Octal Number System
Base = 8
  8 digits { 0, 1, 2, 3, 4, 5, 6, 7 }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
8
1
1/8
64
1/64
5
1
2
7
4
5 *82+1 *81+2 *80+7 *8-1+4 *8-2
=(330.9375)10
(512.74)8

## Slide 8: Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Bit x Weight”
Formal Notation
Groups of bits 4 bits = Nibble
8 bits = Byte
1
0
-1
2
-2
2
1
1/2
4
1/4
1
0
1
0
1
1 *22+0 *21+1 *20+0 *2-1+1 *2-2
=(5.25)10
(101.01)2
1 0 1 1
1 1 0 0 0 1 0 1

## Slide 9: Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
16
1
1/16
256
1/256
1
E
5
7
A
1 *162+14 *161+5 *160+7 *16-1+10 *16-2
=(485.4765625)10
(1E5.7A)16

## Slide 10: Common Powers
2-3 = 0.125 2-2 = 0.25 2-1 = 0.5 20 = 1 21 = 2 22 = 4 23 = 8 24 = 16 25 =32 26 = 64 27 = 128 28 = 256 29 = 512 210 = 1024 211 = 2048 212 = 4096
160 = 1 = 20 161 = 16 = 24 162 = 256 = 28 163 = 4096 = 212
210 = 1024 = 1 K 220 = 1048576 = 1 M (1 Megabits) = 1024 K = 210 x 210 230 = 1073741824 = 1 G (1 Gigabits)

## Slide 11: Binary Codes
One Binary Digit (one bit) can take on values 0, 1. We can represent TWO values:
(0 = hot, 1 = cold), (1 = True, 0 = False), (1 = on, 0 = off) Two Binary digits (two bits) can take on values of 00, 01, 10, 11. We can represent FOUR values:
(00 = hot, 01 = warm, 10 = cool, 11 = cold)
Three Binary digits (three bits) can take on values of 000, 001, 010, 011, 100, 101, 110, 111. We can represent 8 values 000 = Black, 001 = Red, 010 = Pink, 011 = Yellow, 100 = Brown, 101 = Blue, 110 = Green , 111 = White

## Slide 12: Contd..
N bits (or N binary Digits) can represent 2N different values
(for example, 4 bits can represent 24 or 16 different values) N bits can take on unsigned decimal values from 0 to 2N-1.
Codes usually given in tabular form
000 001 010 011 100 101 110 111
black red pink yellow brown blue green white

## Slide 13: Addition
Decimal Addition
5
5
5
5
+
0
1
1
= Ten ≥ Base
1
1
Carry

## Slide 14: Binary Addition
Column Addition
1
0
1
1
1
1
1
1
1
1
0
+
0
0
0
0
1
1
1
≥ (2) 1 0
1
1
1
1
1
1
= 61
= 23
= 84

## Slide 15: Binary Subtraction
Borrow a “Base” when needed
0
0
1
1
1
0
1
1
1
1
0
−
0
1
0
1
1
1
0
= (10)2
2
2
2
2
1
0
0
0
1
= 77
= 23
= 54

## Slide 16
Binary Multiplication
Bit by bit
0
1
1
1
1
0
1
1
0
0
0
0
0
0
0
1
1
1
1
0
1
1
1
1
0
0
0
0
0
0
1
1
0
1
1
1
0
x

## Slide 17
Summary
Value of number is determined by multiplying each digit by a weight and then summing
Binary Number System has Radix = 2
Decimal Number System has radix = 10
Octal number system has radix = 8
Hexadecimal number system has radix = 16