## Slide 1
Basics of Memories

## Slide 2: Lecture 43 Basic concepts of Concepts of PLA, PAL, CPLD, FPGA
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of programmable logic devices
  Acquire the knowledge of PLA, PAL, CPLD, FPGA

## Slide 4: Topics
  Programmable Logic Devices

## Slide 5: PLD
Problems by Using Basic Gates
Many components on PCB:
  As no. of components rise, nodes interconnection complexity grow exponentially
  Growth in interconnection will cause increase in interference, PCB size, PCB design cost, and manufacturing time

## Slide 6: PLD
The purpose of a PLD device is to permit elaborate digital logic designs to be implemented by the user in a single device
Can be erased electrically and reprogrammed with a new design, making them very well suited for academic and prototyping
Types of Programmable Logic Devices
SPLDs (Simple Programmable Logic Devices)
  ROM (Read-Only Memory)
  PLA (Programmable Logic Array)
  PAL (Programmable Array Logic)
  GAL (Generic Array Logic)
CPLD (Complex Programmable Logic Device)
FPGA (Field-Programmable Gate Array)

## Slide 7: PLD
The first three varieties are quite similar to each other:
  They all have an input connection matrix, which connects the inputs of the device to an array of AND-gates.
  They all have an output connection matrix, which connect the outputs of the AND-gates to the inputs of OR-gates which drive the outputs of the device.
The gate array is significantly different and will be described later.

## Slide 8: PLD
The differences between the first three categories are these:
  In a ROM, the input connection matrix is hardwired. The user can modify the output connection matrix.
  In a PAL/GAL the output connection matrix is hardwired. The user can modify the input connection matrix.
  In a PLA the user can modify both the input connection matrix and the output connection matrix.

## Slide 9: General structure of PLDs

## Slide 10
Logic gates
and
programmable
switches
Inputs
(logic variables)
Outputs
(logic functions)
PLD as a Black Box

## Slide 11: Buffer/inverter
(a) Symbol. (b) Logic equivalent.

## Slide 12: Programming by blowing fuses.
(a) Before programming. (b) After programming.

## Slide 13: OR - PLD Notation

## Slide 14: AND - PLD Notation

## Slide 15
Summary
As number of components rise, nodes interconnection complexity grow exponentially
The purpose of a PLD device is to permit elaborate digital logic designs to be implemented by the user in a single device
Can be erased electrically and reprogrammed with a new design, making them very well suited for academic and prototyping