## Slide 1
Basics of Memories

## Slide 2: Lecture 44 Basic concepts of Concepts of PLA and PAL
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Acquire the knowledge of programmable logic array
  Acquire the knowledge of programmable array logic

## Slide 4: Topics
PLA
PAL

## Slide 5: Array Logic
Array logic has two major forms:
  Programmable logic devices (PLDs)
  Field programmable gate arrays (FPGAs)
Programmable logic devices (PLDs)
  These are examples of uncommitted logic
  Forms include:
    PLA – programmable logic array
    PAL – programmable array logic
    GAL – generic array logic
    EPLD – erasable programmable logic device
    CPLD – complex programmable logic device

## Slide 6: Programmable logic array (PLA)
  Has an array of inverters, AND gates and OR gates
  Can implement any logic function (given limits on numbers of inputs and outputs)
  Example: consider a system with four inputs A, B, C and D and three output X, Y and Z, where

## Slide 7
  Use to implement circuits in SOP form
  The connections in the AND plane are programmable
  The connections in the OR plane are programmable
f
1
AND plane
OR plane
Input buffers
inverters
and
P
1
P
k
f
m
x
1
x
2
x
n
x
1
x
1
x
n
x
n
Programmable Logic Array (PLA)

## Slide 8: The structure of a simple PLA

## Slide 9: Contd..
The PLA programmed to give the required output functions
  The device is programmed by blowing fusible links at the various interconnection points

## Slide 10
  PLAs come in various sizes
    Typical size is 16 inputs, 32 product terms, 8 outputs
      Each AND gate has large fan-in  this limits the number of inputs that can be provided in a PLA
      16 inputs  316 = possible input combinations; only 32 permitted (since 32 AND gates) in a typical PLA
      32 AND terms permitted  large fan-in for OR gates as well
        This makes PLAs slower and slightly more expensive than some alternatives to be discussed shortly
      8 outputs  could have shared minterms, but not required
Limitations of PLAs

## Slide 11
  Also used to implement circuits in SOP form
  The connections in the AND plane are programmable
  The connections in the OR plane are NOT programmable
f
1
AND plane
OR plane
Input buffers
inverters
and
P
1
P
k
f
m
x
1
x
2
x
n
x
1
x
1
x
n
x
n
fixed connections
Programmable Array Logic (PAL)

## Slide 12
f
1
P
1
P
2
f
2
x
1
x
2
x
3
AND plane
P
3
P
4
f1 = x1x2x3'+x1'x2x3
f2 = x1'x2'+x1x2x3
Example Schematic of a PAL

## Slide 13
  PALs have the same limitations as PLAs (small number of allowed AND terms) plus they have a fixed OR plane  less flexibility than PLAs
  PALs are simpler to manufacture, cheaper, and faster (better performance)
  PALs also often have extra circuitry connected to the output of each OR gate
    The OR gate plus this circuitry is called a macrocell
Comparing PALs and PLAs

## Slide 14
Summary
Array logic has two major forms:
  Programmable logic devices (PLDs)
  Field programmable gate arrays (FPGAs)
  PLA has an array of inverters, AND gates and OR gates
  PLA’s are used to implement circuits in SOP form
  PAL’s are also used to implement circuits in SOP form
  PALs are simpler to manufacture, cheaper, and faster (better performance)