## Slide 1
Introduction to Digital Electronics

## Slide 2: Lecture 6 Number System
Lecture delivered by:
Deepak V.

## Slide 3: Objectives
At the end of this lecture, student will be able to:
  Convert Octal to Binary
  Acquire the knowledge of Hexadecimal to Binary conversion
  Explain the conversion of Decimal to Octal
  Convert Decimal to Hexadecimal conversion
  Acquire the knowledge of Binary to Octal conversion
  Explain the conversion of Binary to Hexadecimal
  Acquire the knowledge of Octal to Hexadecimal conversion
  Convert Hexadecimal to Octal conversion

## Slide 4: Topics
Octal to Binary conversion
Hexadecimal to Binary conversion
Decimal to Octal conversion
Decimal to Hexadecimal conversion
Binary to Octal conversion
Binary to Hexadecimal conversion
Octal to Hexadecimal conversion
Hexadecimal to Octal conversion

## Slide 5
Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 6: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation
Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 7: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 8: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation
Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 9: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 10
Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder
Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228

## Slide 11: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 12: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder
Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4

## Slide 13: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 14: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits
Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 15: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 16: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits
Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 17
Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 18
Octal to Hexadecimal
Technique
  Use binary as an intermediary
10768 = ?16
1 0 7 6
001 000 111 110
2 3 E
10768 = 23E16
Example

## Slide 19
Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 20
Hexadecimal to Octal
Technique
  Use binary as an intermediary
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1 7 4 1 4
1F0C16 = 174148
Example

## Slide 21
Summary
Octal to Binary
Convert each octal digit to a 3-bit equivalent binary representation
Convert each hexadecimal digit to a 4-bit equivalent binary representation
Hexadecimal to Binary
Divide by 8
Keep track of the remainder
Decimal to Octal
  Divide by 16
  Keep track of the remainder
Decimal to Hexadecimal